## Slide 1: mRNA vaccine production
By,
Anirudh Veliyur(20CHE191)
Shauryaraj Jilkar(20CHE172)

## Slide 2
Principle

## Slide 3
DNA Sequencing
Plasmid Insertion
Transcription by RNA polymerase
Purification by chromatography or tangential flow filtration
Protection in lipid bilayer
Delivery
Sequence of operations in the manufacturing process

## Slide 4
Description of the manufacturing process
DNA Sequencing
Production of mRNA-based therapeutics and vaccines typically or commonly begins with a pDNA template that contains a DNA-dependent RNA polymerase promoter and the corresponding sequence for the mRNA construct.

## Slide 5
2) Plasmid insertion
pDNA Amplification
Linearization of pDNA

## Slide 6
3) Transcription by RNA polymerase
In-vitro transcription
Enzymatic capping

## Slide 7
4) Purification of mRNA

## Slide 8
5) Protection in bilipid layer & delivery

## Slide 9
Enzymatic data from Michaelis-Menten Plot
Data set 1 |  |  | 
[NTP]tot, μM | [Enz]tot, μM | Velocity, μM·∙min-­‐1 | [NTP]/Vel
0.02 | 0.04 | 0.61 | 0.032787
0.04 | 0.04 | 1.03 | 0.038835
0.06 | 0.04 | 1.15 | 0.052174
0.08 | 0.04 | 1.25 | 0.064
0.12 | 0.04 | 1.23 | 0.097561
0.16 | 0.04 | 1.34 | 0.119403
Chart: Hanes-Wolfe plot(Data Set 1)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.12 | 0.16
 | 0.032787 | 0.038835 | 0.052174 | 0.064 | 0.097561 | 0.1194
Vmax | 1.529754
Km | 0.023252
Kcat | 38.24384

## Slide 10
Enzymatic data from Michaelis-Menten Plot
Data set 2 |  |  | 
[NTP]tot, μM | [Enz]tot, μM | Velocity, μM·∙min-­‐1 | [NTP]/Vel
0.02 | 0.08 | 0.67 | 0.029851
0.04 | 0.08 | 1.31 | 0.030534
0.06 | 0.08 | 1.9 | 0.031579
0.08 | 0.08 | 2.25 | 0.035556
0.12 | 0.08 | 2.49 | 0.048193
0.16 | 0.08 | 2.83 | 0.056537
Chart: Hanes-Wolfe plot(Data set-2)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.12 | 0.16
 | 0.029851 | 0.030534 | 0.031579 | 0.035556 | 0.048193 | 0.056537
Vmax | 4.844961
Km | 0.107558
Kcat | 60.56202

## Slide 11
Optimum conditions
Chart: Activity(Kcat) vs Temp
| 22 | 27 | 32 | 37 | 42
Activity(Kcat) vs Temp | 3.3 | 7.7 | 16.5 | 28.3 | 55.2
Chart: Incorporation of CMP32 vs pH
| 6.1 | 7 | 7.8 | 8 | 8.1999999999999993 | 8.9
 | 5.33 | 25.42 | 38.23 | 41.33 | 38.61 | 34.44
Chart: Incorporation of CMP32 vs Molarity of 'metal' ion
| 0.2 | 0.45 | 0.7 | 1.6
Mg2+ | 3.3 | 4.2 | 5.9 | 5.1
Mn2+ | 5.8 | 7 | 7.2 | 6.85 | 6
Temp range:- 38 - 42 °C
pH range:- 7.8 - 8.2
Mg2+ conc :- 8x10-3 M
Mn2+ conc :- 2x10-3 M

## Slide 12
Mass Balance

## Slide 13
Equilibrium constraints

## Slide 14
Kinetic expressions

## Slide 15
Differential equations

## Slide 16
Process Conditions
1) Preparation of pDNA and production
Temperature:- 37°C
PCR amplification
Cell disruption through alkaline lysis at pH 12
        pDNA precipitation with high-salt buffer (sodium or potassium acetate at concentration of 0.7 M–3.0 M and pH ~5–7.5, with/without 0.8–1.5% CaCl2) in the presence of a detergent (1% SDS)

## Slide 17
2) Linearization of pDNA
pDNA + restriction enzyme in a reaction buffer and incubation at 37 °C for 4 hours.
Reaction can be stopped by addition of EDTA or heat inactivation at 65 °C.
Tangential flow filtration and chromatography are then performed to remove impurities like restriction enzyme, BSA, DNA fragments, endotoxins.

## Slide 18
3) In-vitro transcription
DNA template at 10-70 nM
NTPs at 0.5-10 mM
T7 RNA polymerase at 1000-12000 U/mL
Magnesium at 12-60 mM
Buffer (HEPES or Tris) at a pH of 7-8.5
Pyrophosphatase at 1 U/mL
In-vitro transcription reaction is allowed to proceed, for example, under constant mixing at 37°C for 4 hours.

## Slide 19
4) Capping of the RNA
S-adenosylmethione chloride*2HCl is dissolved at 20mM in 5mM HC1 10/90 v/v% ethanol/ water as a prepared stock.
The final IX buffer conditions consist of the following: 50mM Tris HCl pH 8, 5mM KC1, 1mM MgC12, and 1mM dithiothreitol.
The reaction is run under constant mixing at 37°C for 2 hours.

## Slide 20
5) Purification and Concentration of product mRNA
Ethanol precipitation is carried out, most salts and small organic molecules are soluble in 70% ethanol.
Lithium chloride is used for precipitation of RNA as it can effectively precipitate RNA selectively and not DNA, carbohydrates and proteins.
Stock concentration of LiCl is 8M and working concentration required is 0.8M.

## Slide 21
6) LNP Delivery
Modified ethanol dilution process
Lipid components: (DSPC: cholesterol: PEG-DMG 2000: DLinDMA) 10:48:2:40 molar percent respectively.
An 8:1 N:P molar ratio (nitrogen on DlinDMA to phosphate on RNA)
100 mM citrate buffer (pH 6)
After 1 h equilibration at room temperature, the mixture was further diluted with 1:1 vol/vol citrate buffer.
LNPs obtained were concentrated and dialyzed against 1× PBS using tangential flow filtration (TFF) with polyethersulfone (PES) hollow fiber membranes with a 100-kDa pore size cutoff and 20 cm2 surface area.